## Slide 1: Research roadmap for homomorphic encryption
Di Wu, M. Sazadur Rahman, Xin Xin, Mike Borowczak

## Slide 2: Outline
1 Goal
2 Milestone
3 Outcome
4 Resource

## Slide 3: Goal
Education
Research
Engineering
training
Critical thinking
and teamwork
Research
philosophy

## Slide 4: Milestone
Metric
formulation
Workload
profiling
Hardware
design
Algorithm
analysis
Architecture
research
Software
integration
Scheme: BGV, TFHE, CKKS
(all having bootstrapping capability; most costly operations being NTT)
Framework: OpenFHE
(identifying compute/memory bottlenecks; supporting all schemes)
ISA: compute and memory
(CISC/RISC, memory access granularity, flexible conversion)
EDA: Synopsys ASIP
(ISA mapping and design automation)
Formal
verification
Modules:
VLP kernel
Montgomery modular multiplication
etc.
Schedule: dataflow optimization
(mixture of GEMM and NTT)

## Slide 5: Timeline

## Slide 6: HW acceleration with ASIP – Subtasks
Synthetization of Knowledge (SoK)
  Synopsys ASIP Tools
    Understand the complete flow from architecture  compiler  RTL  testbench generation
    Perform the full flow on a prototype designs
    Review the capabilities of ASIP – existing functional blocks, defining custom blocks, etc.
  FHE Building blocks –
    High level – relinearize, rotate, rescale, keyswitch, etc.
    Basic – NTT, iNTT, Reduction, Modular add/mult
HW Acceleration (HWAcc)
  Parameterize the HW
    Understand the system architecture and the microarchitecture from Dr. Di Wu’s team
    Design space exploration - Practical FHE parameter set that is synthesizable
    Chose HW platform – cloud/local FPGA, FPGA spec
    Memory bandwidth acceleration – PIM, HBM, Radix, etc. (if time permits)
  Codify the HW
    HLS (high-level synthesis) based accelerator design for the microarchitectures – C/nML  RTL
    Integrated the microarchitectural blocks for building the overall FHE accelerator module
  Verify the HW
    Perform functional simulation
    Optimize the design to meet specification/constraint
  Configure the HW
    Generate bitstream for FHE accelerator
    Configure the FPGA with the bitstream
    Test the HW for functional and specification correctness

## Slide 7: HW acceleration with ASIP – Timeline
Sub-tasks | Oct-23 | Nov-23 | Dec-23 | Jan-23 | Feb-23 | Mar-23 | Apr-23 | May-23 | Jun-23 | Jul-23 | Aug-23 | Sep-23
SoK (a) (i) |  |  |  |  |  |  |  |  |  |  |  | 
SoK (a) (ii) |  |  |  |  |  |  |  |  |  |  |  | 
SoK (a) (iii) |  |  |  |  |  |  |  |  |  |  |  | 
SoK (b) (i) |  |  |  |  |  |  |  |  |  |  |  | 
SoK (b) (ii) |  |  |  |  |  |  |  |  |  |  |  | 
HWAcc (a) (i) |  |  |  |  |  |  |  |  |  |  |  | 
HWAcc (a) (ii) |  |  |  |  |  |  |  |  |  |  |  | 
HWAcc (a) (iii) |  |  |  |  |  |  |  |  |  |  |  | 
HWAcc (a) (iv) |  |  |  |  |  |  |  |  |  |  |  | 
HWAcc (b) (i) |  |  |  |  |  |  |  |  |  |  |  | 
HWAcc (b) (ii) |  |  |  |  |  |  |  |  |  |  |  | 
HWAcc (c) (i) |  |  |  |  |  |  |  |  |  |  |  | 
HWAcc (c) (ii) |  |  |  |  |  |  |  |  |  |  |  | 
HWAcc (d) (i) |  |  |  |  |  |  |  |  |  |  |  | 
HWAcc (d) (ii) |  |  |  |  |  |  |  |  |  |  |  | 
HWAcc (d) (iii) |  |  |  |  |  |  |  |  |  |  |  | 
Research
Outcome
Notes: Synthetization of Knowledge (SoK)
  Synopsys ASIP Tools
    Understand the complete flow from architecture  compiler  RTL  testbench generation
    Perform the full flow on a prototype designs
    Review the capabilities of ASIP – existing functional blocks, defining custom blocks, etc.
  FHE Building blocks –
    High level – relinearize, rotate, rescale, keyswitch, etc.
    Basic – NTT, iNTT, Reduction, Modular add/mult
HW Acceleration (HWAcc)
  Parameterize the HW
    Understand the system architecture and the microarchitecture from Dr. Di Wu’s team
    Design space exploration - Practical FHE parameter set that is synthesizable
    Chose HW platform – cloud/local FPGA, FPGA spec
    Memory bandwidth acceleration – PIM, HBM, Radix, etc. (if time permits)
  Codify the HW
    HLS (high-level synthesis) based accelerator design for the microarchitectures – C/nML  RTL
    Integrated the microarchitectural blocks for building the overall FHE accelerator module
  Verify the HW
    Perform functional simulation
    Optimize the design to meet specification/constraint
  Configure the HW
    Generate bitstream for FHE accelerator
    Configure the FPGA with the bitstream
    Test the HW for functional and specification correctness

## Slide 8: Outcome
Education
Research
Training:
From fellows
to experts
Course:
Materials from
Practices
Product:
Impact GPU and
ASIP in 4 years
Workflow:
Architecture->
verification->
ASIP
Publication:
6 papers
in 3 years
Whitepaper,
computing,
memory,
ASIP,
system,
formal method,
etc.
End-to-end workflow with full-stack EDA support
AMD machines, ASIP toolchain, developing environment, etc.
Collect, synthesize best practices and include them in courses
Close integration,
Better performance, security, etc.

## Slide 9: Resource
1 AMD server
with 1~2 GPUs
Remote env access
ASIP workshop